OUTPUT:
Startup and Basic Operation

The synth-duo branch of OUTPUT is designed for two networked performers on separate computers. Audio for both performers is synthesized in parallel in both the master and client patches, and control data is transmitted between performers using TCP on port 57120. If the performers are on separate networks, the master performer will need to create a port rule on their router to allow the client connection request.

The following guide is minimal, but provides enough information to get started with creating music, recording automation data, saving presets, and saving complex scenes.

1. Pure Data Installation and Dependencies
  1. OUTPUT requires Pure Data version 0.50-0 or greater
  2. OUTPUT also requires the following externals, which you can install via the Help/Find externals menu option
    1. hcs
    2. motex
    3. ofelia
    4. tof
    5. zexy

1. Startup
  1. One performer should be designated the master and the other client
  2. Each performer should open the OUTPUT-master.pd or OUTPUT-client.pd correspondingly

1. MIDI Control
  1. OUTPUT has extensive MIDI mappings to control its GUI
    1. See doc/MIDI-mapping.ods for a detailed breakdown of each MIDI CC index, and assign faders and knobs on your MIDI controller(s) accordingly
    2. If you own both the Korg nanoKONTROL2 and nanoKONTROL Studio controllers, you can load the following mapping preset files to use a pre-designed layout
      1. doc/OUTPUT-settings.nktrl2_data
      2. doc/OUTPUT-settings.nktrl_st_set

1. Computer Keyboard Control
  1. OUTPUT also has extensive computer keyboard mappings available as optional methods to control various GUI elements
    1. See doc/computer-keyboard-mapping.ods for a detailed breakdown of each key
  2. Computer keyboard mapping is disabled by default. To activate it, click the toggle box labeled “k” in the lower section of the main patch window

1. Signal Plots
  1. OUTPUT provides a basic waveform plot of each performer’s signals
    1. Click the “visuals” button in the lower section of the main patch window to show these plots

1. Remote Connection
  1. An OUTPUT session requires a network connection between the client and master
  2. The client can connect to the master by entering the master’s public IP address in the red panel at the bottom of the OUTPUT-client.pd patch window.
    1. To enter an IP, you must click on the IP field, type the IP, then hit enter
    2. To make the connection, click the “connect” toggle
    3. If connection is successful, the red panel will turn green

1. Algorithm Players
  1. Each OUTPUT performer has access to two bytebeat algorithm players for generating audio
  2. For both the master and client performer, the two algorithm players will be referred to below as A and B
  3. Each algorithm player has dozens of GUI controls shown in the main patch window
    1. The upper control panel row is for player A
    2. The lower control panel row is for player B
  4. Performers can toggle active MIDI control of their A or B algorithm player using assigned MIDI controls or the computer keyboard’s space bar
    1. The currently active algorithm player’s control panel will be highlighted with a pink panel
    2. When a given algorithm player is active, MIDI controls and the computer keyboard affect the parameters of that player only

1. Player Parameters
  1. The primary algorithm player GUI elements in the control panel affect many different parameters
    1. Gain
    2. Muting
    3. Algorithm choice
      1. OUTPUT includes 123 bytebeat algorithms, which can be selected with the algo-select number box via indices 0-122
      2. These algorithms are stored in doc/outputAlgorithms.txt, and users are free to edit, add, or remove the contents
        1. For consistent results on both the master and client side, the contents of this file should be identical on both performers’ computers
    4. Bit depth
      1. The output of bytebeat algorithms can be interpreted at any bit depth between 1 and 24
    5. Reverb dry/wet and liveness
    6. Interpolation
      1. The raw output of bytebeat algorithms is often harsh and has jagged waveform edges. Turn interpolation on in order to smooth these out and get a warmer sound
    7. ASR keyboard
      1. Each algorithm player produces signal constantly. The ASR keyboard feature only allows signal through when a MIDI keyboard note is active
      2. The GUI slider just above the ASR keyboard toggle controls the attack/release time of this process
    8. Spatial panning position
    9. Spatial panning width
      1. Spatial panning position and width function as expected
      2. By default, the synth-duo branch of OUTPUT launches in stereo mode, indicated by the active toggle labeled “s” in the lower right of the main patch window
      3. Deactivating this stereo toggle enables 8-channel surround mode
    10. Time location
      1. Signal produced by a given bytebeat algorithm can vary tremendously depending on the current time position
      2. The GUI number box labeled “t” indicates the current time position in samples
      3. The GUI number box labeled “m” controls time position in minutes
    11. Time direction
      1. Bytebeat algorithm players play forwards in time by default, but can play backwards when the GUI toggle labeled “t-rev” is activated
    12. Loop record
      1. It is possible to loop playback between a desired start and end time point
      2. Activating the GUI toggle labeled “loopRec” sets the start time of the loop, and deactivating it sets the end time
        1. looping playback begins immediately after the end time is set
      3. To clear a loop, click the purple button in the same region of the control panel

    1. Tempo
      1. The playback speed of an algorithm player is controlled with the tempo setting
      2. Tempo can range from 1BPM to 240BPM, however the definition of a “beat” varies from one bytebeat algorithm to the next
      3. This parameter is better described as “speed”, and future versions will likely implement this change in label
      4. Note that tempo (speed) changes affect both pitch and speed, so this parameter can also be thought of as “pitch”
        1. The technical parameter behind this aspect of controlling bytebeat algorithm playback is simply sampling rate
        2. Choosing one description of this parameter is difficult because some bytebeat algorithms produce periodic waveforms that simply change in pitch when the sampling rate changes, while other algorithms produce rhythmic and melodic patterns. In the latter case, changing the sampling rate affects both the tempo and key of the result
    2. Pitch bend
      1. Slight changes to the tempo parameter can be made using the pitch bend wheel on your MIDI keyboard
    3. Pitch bend range
      1. The range of pitch/tempo bending can be set from 1-51BPM
    4. Tempo sync to another algorithm player
      1. Lock tempo with any of the other algorithm players using the 4-element GUI radio button
        1. There are 4 players (0 and 1 for master; 2 and 3 for client) and 4 corresponding radio buttons
    5. Time sync to another algorithm player
      1. Jump to the same time location as any other algorithm player using a similar 4-element GUI radio button
      2. If tempo is already locked to a given player, jumping to that player’s time location will keep time flow parallel between the two players
    6. Clone settings of another algorithm player
      1. Clone all settings of another algorithm player using this 4-element GUI radio button to exactly reproduce the output of another player
      2. Note that any parameter changes (manual or automated) will break exact reproduction

1. Algorithm Parameters
  1. The right side of each algorithm player’s control panel contains GUI controls to adjust the free parameters of the active algorithm
  2. The number of free parameters varies from algorithm to algorithm, but the maximum is 10
  3. The +/- buttons above each free parameter number box increment and decrement that parameter for fine tuning
  4. The +/- buttons will be colored yellow for all valid free parameters of the active algorithm
    1. Adjusting invalid free parameter controls will have no effect

  1. The button below each free parameter GUI control will randomize that parameter according to the current random range in the number box just below
  2. The “randomize” button in the lower left randomizes all free parameters at once

1. Preset Loading and Saving
  1. The “save” and “load” buttons at the right of each algorithm player’s control panel save and load presets containing the following algorithm player settings:
    1. algorithm choice
    2. free parameter values
    3. bit depth
    4. sampling rate (i.e., tempo/pitch)
    5. time location
    6. loop points
    7. time direction
    8. interpolation
  2. Preset files are human-readable and -editable, and are stored in the algo-presets directory by default
  3. The purple “r” button refreshes the most recently loaded preset
  4. The “load” button activates a popup menu listing all preset files in the algo-presets directory
  5. The “*” button to the right brings up a system dialog for navigation to any directory and preset file choice

1. Automation Recording
  1. Parameter automation is a powerful tool for creating dynamic audio from otherwise repetitive algorithmic output
  2. Automation is only possible when using a MIDI controller
  3. To record automation data for a given parameter:
    1. Move the MIDI control for the parameter you wish to record
    2. Press and hold the MIDI control button assigned to automation record (this is MIDI CC 124: see doc/MIDI-mapping.ods)
    3. While the automation record MIDI control button is depressed, move the MIDI control for the parameter you wish to record
    4. To stop recording, release the automation record MIDI control button and stop moving the MIDI control for the parameter you were recording
    5. Automation data playback begins immediately, and will loop indefinitely
    6. To stop automation playback, move the MIDI control for the automated parameter

1. Scene Loading and Saving
  1. Scene saving captures all aspects of the performer’s algorithm players except gain
    1. When a scene is loaded, current gain levels of players A and B will not change.
      1. This allows silent loading of a scene to avoid unintentionally sudden changes
  2. The red and green buttons in the bottom of the main patch window save and load scenes respectively
  3. Upon saving, a new directory is created in the OUTPUT/scenes directory
  4. Each scene directory contains algorithm player presets for players A and B, automation data for players A and B, and additional scene data.
    1. Apart from the algorithm player presets, these files are not designed to be edited